## Slide 1: Intro to 3D Printing for BME
Attendance Form

## Slide 2: What is 3D Printing?
Additive Manufacturing
Subtractive Manufacturing
Stereolithography (SLA)
Fused Deposition Modeling (FDM)

## Slide 3
FDM Printer Terms
Filament
Extruder
(Heated) Nozzle
(3D) Print
(Print) Bed
“I love the filament fumes!”
“The extruder isn’t extruding”
“The Print came out wrong”
“The nozzle is clogged”
“The print didn’t stick to the bed”

## Slide 4
FDM Printer Anatomy

## Slide 5
The UH BMES Printer
Model: Ender 3 V2
Area: 220 [mm] x 220 [mm] x 250 [mm]
Resolution: 0.1 [mm] – 0.4 [mm]
Max. Nozzle Temp: 250˚C / 482˚F
Max. Bed Temp: 110˚C / 230˚F
Heat up Time: 5 minutes

## Slide 6
3D Printing Process
Modeling
Slicing
Printing
.dwg
.stp
.stl
.3mf
.gcode
.x3g
Printer Screen

## Slide 7: Designing a Model
3D Printing-Specific Considerations
Horizontal plane has more resolution than vertical plane
Maximize Bed Contact
  Minimizes Support Structures
Fillet/Chamfer edges when possible
  Prevents warping due to cooling and thermal stress
3D Computer-Aided Design (CAD) Programs
TinkerCAD
FreeCAD
Autodesk Products
  Inventor
  Fusion
  Provided to UH Students
SOLIDWORKS

## Slide 8: What is Slicing?
Slicing: Converting a 3D model into a format that 3D printers can understand
Choose a slicing software
  Creality
  Slic3r
  Cura
  KISSlicer
Import an STL file
Adjust printing settings
Export as design G-code
GENERAL STEPS

## Slide 9
Infill
Infill = Internal structure of a 3D-printed part (solid = 100% infill)
Density Considerations:
  5-10%: Prototyping
  10-20%: Standard
  30-50%: Strong
Patterns:
  Line: Fast and cost-effective
  Grid: Fast and Rigid
  Gyroid: Even strength distribution and allows for filling
  Concentric: Increases flexibility

## Slide 10
Layer Height
“Vertical Resolution”
Max =
Affects:
  Surface Roughness
  Vertical Text Quality
  Overhang
Trade-off between strength and quality

## Slide 11
Wall Thickness
Horizontal = Wall/Shell Thickness
  Vertical = Top/Bottom Thickness
Types of Walls:
  Outer (first)
  Inner (not Outer)
Should be a multiple of (at least 2x) nozzle diameter
Disadvantage of increasing wall thickness is wasting time/material

## Slide 12
Line
Width
Default = nozzle diameter
Range = ± 20% nozzle diameter
Many types
  Outer Wall Line Width
    Surface features that are ≤ nozzle diameter
  Initial Layer Line Width
  Infill Line Width
    Increases Strength without affecting time
Front
Front
Front
Front

## Slide 13
Support Material
Supports: Structures that prop up the model
  Applicable to overhangs >45˚ from vertical by default
Settings:
  XY Distance
  Z Distance
  Overhang Angle
E

## Slide 14
Bed Adhesion
Maximize First Layer Surface Area
Adhesion prevents warping
First Layer Adhesion Options:
  None
  Skirt: Line around the model
  Brim: Flat surface around model
  Raft: Thick platform below model

## Slide 15
Inaccuracy in Printing
Sources of Inaccuracy
Part Cooling
Minimum Feature Size
File Conversion Errors
Lack of Calibration
Over/Under-extrusion
Solutions to Inaccuracy
Calibrate the Printer
Adjust Design
Adjust Slicing Parameters

## Slide 16
Adjusting Design
Solutions to Inaccuracy
Keep printer tolerance in mind:
FDM ≈ ±0.5% (min. = ±0.5 mm)
Choose a type of fit
Clearance Fit
Interference Fit
Transition Fit
Horizontal > Vertical

## Slide 17
Adjusting Slicing
Solutions to Inaccuracy
Decrease Layer Height
Decrease Speed / Acceleration / Jerk
< 0.6 mm/s, 3000 mm/s2, 15 mm/s
Other options:
Outer before Inner walls, coasting

## Slide 18: Thank you for Attending!
Resources on our Website!